## Slide 1
Sonic Log Predictions: XGBoost and Wavelet Transform
Exploring Techniques, and Applications for reliable sonic log predictions.
By: Katherine Grey

## Slide 2
Introduction to Sonic Log Predictions
Machine learning models enhance accuracy by predicting missing sonic log data. Ensemble methods best suited for this problem
Machine Learning Solutions
Inaccurate sonic log data can lead to significant financial losses in oil extraction.
Challenges of Incomplete Data
Sonic log data is crucial for maximizing oil production during drilling operations.
Significance of Sonic Logs
1
Sonic Log Predictions: Innovations and Insights
Notes: Sonic logs are used in various drilling operations to reveal key features of the ground that will be drilled. Features like porosity, elastic modulous,. This is done by probigating ultrasonic waves in the ground and then calculating the delta T or time of flight of the returning wave.

## Slide 3
Cost Implications of Sonic Logs
Sonic Log Costs
The cost of generating sonic logs can reach tens of thousands of dollars per bore.
Financial Risks of Gaps
Inaccurate predictions can result inefficient and costly productions from reservoirs.
Savings from Accuracy
Accurate predictions of sonic logs can lower operational costs significantly.
3
Sonic Log Predictions: Innovations and Insights

## Slide 4
Traditional vs. Machine Learning Approaches
Machine learning models can predict missing data, significantly reducing costs.
They improve accuracy in sonic log predictions, especially with techniques like XGBoost.
Wavelet transformation enhances the model's ability to identify complex relationships.
This approach allows for better resource allocation and more frequent data analysis.
Machine Learning Models
Generating sonic logs is costly, often exceeding tens of thousands of dollars per log.
These methods frequently lead to inaccuracies due to missing or incomplete data.
Traditional approaches rely on experimental formulas that may not capture complex relationships.
Overall, they are less efficient in resource allocation and data analysis.
Traditional Methods
4
Sonic Log Predictions: Innovations and Insights

## Slide 5
Key Features of Sonic Logs
Neutron measurement in dec.
It determines the hydrogen content in the formation.
CNC
Gamma Ray measurement in API.
It indicates the presence of shale.
GR
Deep Resistivity measurement in Ohm/m.
It evaluates the formation's conductivity.
HRD
Medium Resistivity measurement in Ohm/m.
It provides insights into fluid content.
HRM
Caliper measurement in inches.
It assesses the borehole diameter.
CAL
2
Sonic Log Predictions: Innovations and Insights

## Slide 6
Pearson and Kendall methods were employed to assess correlations among features.
Pearson is ideal for linear relationships, while Kendall handles non-linear relationships effectively.
Utilize Pearson and Kendall Methods
Three correlation matrices were generated to explore feature relationships.
The pandas pd.corr() function facilitated the initial correlation analysis.
Create Correlation Matrices
A log function was applied to normalize the skewed distributions.
This transformation improved the data's suitability for analysis.
Apply Log Transformations
Histograms and box plots were used to visualize the data distributions.
This analysis revealed skewness and the presence of outliers.
Analyze Skewed Distributions
Instances of -999 were identified as missing values.
These were replaced with NaN to avoid negatively impacting the models.
Handle Missing Values
5
Sonic Log Predictions: Innovations and Insights
Steps in Data Preparation

## Slide 7
Wavelet Transformation in Sonic Log Analysis
Wavelet transformation enhances model accuracy by revealing hidden relationships.
Model Accuracy Enhancement
6
Sonic Log Predictions: Innovations and Insights

## Slide 8
Performance Metrics of the Model
DTC RMSE
The RMSE for DTC is 4.32 pre-wavelet and 5.38 post-wavelet.
1
DTS RMSE
The RMSE for DTS is 23.11 pre-wavelet and 10.35 post-wavelet.
2
Overall RMSE
The overall RMSE is 16.62 pre-wavelet and 8.72 post-wavelet.
3
7
Sonic Log Predictions: Innovations and Insights

## Slide 9
S
W
O
T
Strengths
Weaknesses
Opportunities
Threats
Ethical Considerations in Sonic Log Predictions
Machine learning models enhance the accuracy of sonic log predictions.
They can identify complex relationships in data that traditional methods may overlook.
The reliance on machine learning can lead to a lack of transparency in decision-making processes.
Inaccurate models may produce misleading predictions, impacting operational decisions.
There is potential for cross-industry applications of sonic log predictions, expanding their use beyond oil and gas.
Advancements in machine learning techniques can improve the quality and reliability of predictions.
Ethical concerns arise from the potential misuse of predicted data, leading to harmful consequences.
Regulatory scrutiny may increase as the use of machine learning in critical industries grows.
9
Sonic Log Predictions: Innovations and Insights

## Slide 10
Cross-Industry Utility
Sonic logs improve predictive capabilities in engineering.
Bridge Support Applications
Sonic logs inform subsurface conditions in bridge construction.
Sonic Logs in Pile Driving
Sonic logs assess soil properties during pile driving.
10
Sonic Log Predictions: Innovations and Insights
Applications Beyond Oil and Gas

## Slide 11
Challenges and Limitations
Many features required for the project are not supported in Python 3.13.
This has created challenges in utilizing certain functionalities effectively.
Python Compatibility
Creating virtual environments was necessary to run older Python versions.
This process added complexity and required additional setup time.
Virtual Environments
There is a need to develop a pipeline feature for handling sonic log data with missing attributes.
Current implementations do not adequately address the challenges of incomplete data.
Missing Features
Ensuring model accuracy is crucial when predicting missing sonic log data.
Inaccurate predictions can lead to significant financial consequences.
Model Accuracy
Data quality significantly limits prediction accuracy.
Insufficient data collection in many logs leads to unreliable results.
Data Quality Issues
11
Sonic Log Predictions: Innovations and Insights

## Slide 12
Conclusion and Recommendations
Future work should focus on developing a pipeline feature.
Future Work Recommendations
Wavelet transformation enhanced model performance by revealing stronger correlations.
Wavelet Transformation Benefits
The project improved the accuracy of sonic log data predictions using machine learning.
Project Findings
12
Sonic Log Predictions: Innovations and Insights